## Slide 1
Computational Art – Robotic Picture Weaving
Uri Ziv, Idan Halperin, Gur Elkin
Advisor: Prof. Ohad Ben-Shahar
Department of Computer Science
4. Algorithm and Workflow
5. Results
6. Coming Up Soon: Robotic Implementation
2. Task description
Given a grayscale image, approximate it by drawing a continuous sequence of threads across an arbitrary convex frame of nails. Then, weave it using a robotic arm.
1. Background and Motivation
In recent years it became more common to incorporate computers in the artistic process. For example, image-weaving is a complex task, even for an experienced artist. Our project aspires to automate this process with the help of computer vision, graphics, and robotics.
3. Approach and Concepts
Given two pixels (each representing a nail), define the strand as the set of pixels that resides on the chord between 𝑝 and 𝑞.
The crux of the problem is finding , the sequence of consecutive strands that best approximates the original image when woven across the nail frame. A greedy approach of always picking the strand with minimal mean value was found to yield the best results. formally, we pick the strand such that is the current nail and:
where is the set of all nails in the frame.
Every iteration, brighten the strand’s pixels in the image by a constant and halt when the darkest strand has a mean of .
Step 1 – Preprocessing
Adjust the image to fit the nail frame and calculate the nail positions from a picture of the board.
Step 2 – Strand Sequence Algorithm
StrandSequence(Image, Nails, t, alpha):
1: Sequence ← ().
2: Choose some arbitrary initial nail p.
3: do {
4: s ← darkestStrand(p, Nails, Image).
5: Image[s] ← Image[s] + t.
6: Sequence.append(s).
7: p ← s.otherNail(p).
8: }
9: while (mean(s) < alpha).
10: return Sequence.
Step 3 – Visual Assessment
Asses the algorithm’s output visually, by simulating the weaving process with an animation, and plotting the expected result.
Step 4 – Weaving
Weave the generated approximation of the original image on the physical board using a robotic arm.
Most of the robot’s instruction code is ready to use. Yet, some fine-tuning is still needed before it will be able to perform its complex task; especially when handling delicate movements such as maneuvering between nails. In the upcoming weeks we plan to attain first results of a fully-automated artwork.